## Slide 1
Batch Number : B1
Domain : Internet of Things (IoT) / Wireless Networks
Title : WiFi-Based Attendance and Verification System
Guide : Mr. M Vishnu Prasath AP(SS) AI&DS
Team Members:
Dakshinesh S (727623BAD092)
Jothi Krishnan D N (727623BAD074)
Team member Name (727623BAD036)
Dr. Mahalingam College of Engineering & Technology
Department of Artificial Intelligence & Data Science
23ADP701–PROJECT PHASE - 1
Zeroth Review

## Slide 2: Contents
Problem Statement
Objective
Literature Identified and Findings
Existing Block Diagram
Proposed Block Diagram
Module Description
Requirements
Datasets
References

## Slide 3: Problem Statement
Traditional attendance and access verification relies on biometric scanners (fingerprint or face recognition), which force everyone to physically queue at one checkpoint, causing long waiting times during peak entry hours.
Fingerprint sensors are unreliable with dirt, moisture, or worn ridges, and face-recognition units struggle with masks, poor lighting, or camera angle — leading to repeated failed scans and further delay.
Dedicated biometric hardware is expensive to install and maintain at every entry point, and once biometric data is compromised it cannot be changed or reissued, unlike a password or token.
A single centralized scanner is a bottleneck and a single point of failure: if it malfunctions, the entire attendance or verification process halts for everyone behind it.
There is a need for a low-cost, contactless, and scalable way to verify presence and mark attendance for many people at the same time, without a physical queue at one device.

## Slide 4: Objective
Design a system that verifies attendance and presence using an organization's existing common Wi-Fi network, instead of dedicated biometric scanners.
Eliminate queuing at a single checkpoint by letting many users be verified in parallel, simply by being connected to the shared Wi-Fi access point.
Use network-layer signals — SSID/BSSID association and Wi-Fi RSSI (signal strength) — to confirm that a user's device is physically present within the premises.
Add a lightweight authentication layer (login session/OTP binding) on top of Wi-Fi connectivity so that merely joining the network cannot be used to mark someone else's attendance.
Provide a real-time dashboard for administrators to view attendance logs, flagged exceptions, and analytics.
Reduce hardware cost and maintenance compared to biometric devices, while improving speed, hygiene, and scalability of the verification process.

## Slide 5
Literature Identified and Findings

## Slide 6: 1
WiFi Attend: Real-Time Attendance via Wi-Fi (2025)
Marks attendance by having a user's smartphone connect to a dedicated Wi-Fi hotspot, verifying same-network presence in real time.
Combines a responsive frontend, a backend server, and a Wi-Fi validation module to confirm proximity without extra hardware.
Reports the approach is cost-effective and scalable since institutions already have wireless infrastructure, but flags device authentication and network congestion under high user density as open challenges.
View source ->

## Slide 7: 2
WiFi RSS-Based Automated Attendance System (ACM ICNSS, 2025)
Uses Wi-Fi Received Signal Strength Indicator (RSSI) readings, which are low-cost to capture and more privacy-preserving than camera-based biometrics.
Finds that simple RSSI zone-based systems struggle to validate presence precisely at classroom or room boundaries, creating loopholes for proxy attendance near the edge of coverage.
Proposes pairing Wi-Fi fingerprint-based indoor localization with RSSI zoning to tighten boundary accuracy and reduce spoofing.
View source ->

## Slide 8: 3
Attendance Check System for Wi-Fi Networks with Unlimited Concurrent Connections (Choi et al., 2015)
Issues each verified member a session token; the member's device automatically reports the token to an attendance server once connected to the shared network, with no manual scan needed.
Focuses on detecting whether a device is within range of a known SSID rather than computing an exact distance, avoiding calibration problems of precise RSSI-based ranging.
Shows the approach scales to a large number of simultaneous connections, addressing a key limitation of hardware-bound biometric scanners.
View source ->

## Slide 9: Existing Block Diagram
User Arrives
Waits in Queue
Biometric Scanner (Finger/Face)
Match vs. Database
Pass / Fail Check
Attendance Marked
Entry Denied
Limitation: everyone funnels through a single scanner one at a time, so queue length grows with headcount and any sensor failure or misread halts the whole line.

## Slide 10: Proposed Block Diagram
User Device (Phone/Laptop)
Connects to Common Wi-Fi AP
Wi-Fi Verification Server (SSID/BSSID + RSSI)
Authentication & Anti-Spoofing
Attendance Database
Admin Dashboard / User Notification
Every device already connected to the shared Wi-Fi is checked in parallel by the verification server, so many users are confirmed present at the same time instead of queuing at one scanner.

## Slide 11: Module Description
Wi-Fi Scanning & Connection Module: Detects when a registered user's device associates with the institution's Wi-Fi access point and captures its SSID/BSSID.
Proximity Verification Module: Uses RSSI signal-strength thresholds and access-point mapping to confirm the device is physically within the premises, not connecting remotely.
Authentication Module: Binds each Wi-Fi session to a registered user through a login/OTP step, so simply joining the network cannot mark someone else's attendance.
Anti-Spoofing Module: Detects MAC-address spoofing or duplicate/proxy connections and flags irregular sessions for manual review.
Attendance Database Module: Logs every verified session with timestamp, access-point ID, and status into a central database.
Admin Dashboard Module: Gives coordinators real-time visibility into attendance records, flagged exceptions, and usage analytics.

## Slide 12: Requirements
Hardware Requirements
Wi-Fi access point(s) / router broadcasting the institution's common SSID
Server or cloud instance to host the verification backend
User smartphones / laptops with built-in Wi-Fi (no extra biometric hardware needed)
Software Requirements
Backend: Python (Flask/Django) or Node.js REST API
Database: MySQL / MongoDB for attendance and user records
Frontend: Web or mobile app (React / Flutter) for login and session display
Network layer: Wi-Fi scanning utilities (e.g. iwlist, ARP tables) to capture SSID/BSSID/RSSI
Security: JWT/OTP-based authentication over HTTPS

## Slide 13: Dataset
This is a network-behaviour verification system rather than a computer-vision one, so the working data is largely operational log data rather than a single downloaded dataset:
Access-point logs: SSID/BSSID association records, RSSI values, timestamps, and client MAC addresses captured from the institution's own Wi-Fi router.
User registration data: registered user IDs mapped to device identifiers, collected once during onboarding.
Historical attendance records: used to tune and validate the RSSI proximity threshold (false-accept / false-reject rate).
Public benchmark dataset (for validating the localization technique only): UJIIndoorLoc Wi-Fi fingerprint dataset, UCI Machine Learning Repository.

## Slide 14: References
[1] "WiFi Attend: Real-Time Automated Attendance Management via Wi-Fi," ResearchGate, 2025.
[2] "WiFi Received Signal Strength (RSS) Based Automated Attendance System for Educational Institutions," Proc. 11th Int. Conf. on Networking, Systems and Security (ICNSS), ACM, 2025.
[3] M. Choi, J.-H. Park, and G. Yi, "Attendance Check System and Implementation for Wi-Fi Networks Supporting Unlimited Number of Concurrent Connections," Int. J. Distributed Sensor Networks, 2015.
[4] "UJIIndoorLoc Wi-Fi Fingerprint Dataset," UCI Machine Learning Repository.

## Slide 15: THANK YOU